## Slide 1: KPIs for pavement condition
At the Danish Road Directorate (DRD)
Armand Der-Stepanian, ards@vd.dk Niels Skov Dujardin, nsd@vd.dk

## Slide 2: The Danish Road Directorate
KPIs for pavement condition – The Danish Road Directorate
Numbers and facts about the roads DRD manage.
Infrastructure:
Approximately 5 % of the road network in Denmark
Motorways 1227 km
Other roads 1588 km
Transport:
Approximately 50 % of the road transport in Denmark
Motorways 18,3 billions driven km a year
Other roads 7.2 billions driven km a year
Speed limits
58% of the motorways is 130 km/h
38% of the motorways is 110 km/h
Other roads is typically 80 km/h

## Slide 3: Objective
KPIs for pavement condition – The Danish Road Directorate
Report pavement condition in general terms to non-experts
Report on network level
Pavement condition is based on measurement and not visual inspections
Economy is not part of the report
Do it on one page

## Slide 5: Evenness
KPIs for pavement condition – The Danish Road Directorate
 | GOOD | ACCEPTABLE | MOVING TOWARDS POOR | POOR | Critical
 | No maintenance | Minor maintenance effort | Part of the network need maintenance | Comprehensive maintenance is needed | Urgent need for maintenance
Motorways (IRI, m/km) | 0,8 and below | 0,9 – 1,6 | 1,7 – 2,4 | 2,5 – 3,2 | Above 3,2
Other roads (IRI, m/km) | 1,0 and below | 1,1 – 2,0 | 2,1 – 3,0 | 3,1 – 4,0 | Above 4,1
EVENNESS | Good comfort. No or very few uneven surfaces | Ordinary comfort. Some unevenness due to minor surface damages and/or patches. | Much unevenness is detected. In general the road will be perceived as uneven | Poor comfort, Can lead to safety issues. | Poor comfort with safety issues
Percentage on motorways 2018 | 16,8 % | 81,8 % | 1,2 % | 0,1 % | 0,1 %
Percentage on motorways 2017 | 18,6 % | 80,1 % | 1,2 % | 0,1 % | 0,1 %
Percentage on other roads 2018 | 27,4 % | 65,2 % | 5,2 % | 1,3 % | 0,8 %
Percentage on other roads 2017 | 23,9 % | 69,0 % | 5,2 % | 1,1 % | 0,8 %

## Slide 6: Road Marking visibility
KPIs for pavement condition – The Danish Road Directorate
 | GOOD | ACCEPTABLE | MOVING TOWARDS POOR | POOR | Critical
 | No maintenance | Minor maintenance effort | Part of the network need maintenance | Comprehensive maintenance is needed | Urgent need for maintenance
(Retroreflecsion, mcd/lux/m2) | 150 and above | 130 - 149 | 100 - 129 | 90 - 99 | Below 90
Road Marking Visibility | The road marking appears new | The road marking is clearly visible and do not cause any safety issues | Road markings are visible but the drivers need to be focused. Visibility is problematic in rain and at night | The visibility is poor in any conditions. And will be a safety issue to the road users | Road markings are not visible and an urgent replacement is needed. It is not safe for the road users.
Percentage of road markings on motorways 2018 | 45,3 % | 15,5 % | 21,4 % | 4,9 % | 12,9 %
Percentage of road markings on motorways 2015-17 | 35,2 % | 16,7 % | 27,6 % | 10,7 % | 9,9 %
Percentage of road markings on other roads 2018 | 53,7 % | 15,1 % | 17,7 % | 3,5 % | 10,1 %
Percentage of road markings on other roads 2015-17 | 38,1 % | 18,6 % | 24,8 % | 8,9 % | 9,7 %

## Slide 7
 | GOOD | ACCEPTABLE | MOVING TOWARD POOR | POOR | CRITICAL
 | No maintenance | Minor maintenance effort | Part of the network need maintenance | Comprehensive maintenance is needed | Urgent need for maintenance
BEARING CAPACITY (Remaining structural life based on TSD-screening) | 20 years or above | 15 – 19 years | 5 – 14 years | 0 – 4 years | below 0 years
 | Sufficient Bearing Capacity | Ordinary condition, minor part of the road network needs reinforcement | Reinforcement should be considered when paving a new wearing course | Moderate to high risk of insuficient bearing capacity. Reinforcement needed. | High risk of insuficient bearing capacity. Reinforcement needed.
EVENNESS (IRI, m/km) | 0,8 and below (motorways) 1,0 and below (Other roads) | 0,9 – 1,6 (motorways) 1,1 – 2,0 (Other roads) | 1,7 – 2,4 (motorways) 2,1 – 3,0 (Other roads) | 2,5 – 3,2 (motorways) 3,1 – 4,0 (Other roads) | above 3,2 (motorways) 4,1 – 5,0 (Other roads)
 | Good comfort. No or very few uneven surfaces | Ordinary comfort. Some unevenness due to minor surface damages and/or patches. | Much unevenness is detected. In general the road will be perceived as uneven | Poor comfort, Can lead to safety issues. | Poor comfort with safety issues
RUTTING (depth, mm) | 5 mm and below | 6 – 10 mm | 11 – 15 mm | 16 – 20 mm | above 20 mm
 | No rutting. No risk of aquaplanning | Discomfort when changing lanes. Low risk of aquaplanning | Risk of aquaplaning at heavy rain and high traficspeeds. Discomfort when changing lanes | Risk of aquaplaning and possibility of insuficient bearing capacity. The condition can be a saffety issue | High Risk of aquaplaning and properly insuficient bearing capacity
TEXTUR (MPD, mm) | 0,5 and above | 0,40 – 0,49 | 0,30 – 0,39 | 0,20 – 0,29 | below 0,20
 | Very low risk of insuficient friction | Low risk of insuficient friction | Moderate risk of insufient friction | High risk of incuficient friction | Very high risk of incuficient friction
ROAD MARKING VISIBILITY (mcd/m2/lux) | 150 and above | 130 - 149 | 100 - 129 | 90 - 99 | below 90
 | The road marking appears as new | The road marking is clearly visible and do not cause any safety issues | Road markings are visible but the drivers need to focus. Visibility is problematic in rain and at night | The visibility is poor in any conditions. And will be a safety issue to the road users | Road markings are not visible and an urgent replacement is needed. It is not safe for the road users.

## Slide 8: Single indicators
KPIs for pavement condition – Danish Road Directorate
The Framework for Performance Indicators, PIARC 2004
Single indicators (0-100)
  1 x percentage of the road network in the Good condition
  + 0,75 x percentage of the road network in the Acceptable condition
  + 0,5 x percentage of the road network in the Moving towards poor condition
  + 0,25 x percentage of the road network in the Poor condition
Value of condition indicator Qualitative assessment
  80 – 100 Good
  60 – 79 Acceptable
  40 – 69 Moving towards poor
  20 – 49 Poor
  0 – 19 Critical

## Slide 9: Combined and global indicators
KPIs for pavement condition – Danish Road Directorate
Combined indicators
  Three KPIs from the Danish road standards (normally assessed visually)
  Two new indicators
  Global indicator
 | Bearing capacity | Eveness | Rutting | Texture | Road markings
Remaining life | 50% | 25% | 25% |  | 
Safety |  | 10% | 30% | 30% | 30%
Comfort |  | 50% | 25% |  | 25%
 | Bearing capacity | Eveness | Rutting | Texture | Road Markings
Structural condition | 50% | 25% | 25% |  | 
Functional condition |  | 25% | 25% | 25% | 25%
 | Structural condition | Functional condition
Global condition | 50 % | 50 %

## Slide 11: Further work
KPIs for pavement condition – The Danish Road Directorate
In 2020 a Surface condition indicator will be added that will rely on results from an ARAN9000 with Pavemetrics LCMS2 lasers mounted. At least including:
  Cracks
  Raveling and/or pick outs
  Potholes and delamination
  Patches and sealings
In 2020 friction will be measured on network level to validate that our current texture screening is functioning correct.

## Slide 12
Thank you
Armand Der-Stepanian, ards@vd.dk Niels Skov Dujardin, nsd@vd.dk

## Slide 13
Road surface condition
Cracks raveling potholes Repairs
Cracks raveling potholes Repairs
Friction
Friction